## Slide 1: How Data Is Transported Over Networks Part2 Troubleshooting Router Issues
Notes: Troubleshooting Router Issues
TCP/IP comes with a set of utilities that can help track down most TCP/IP related problems
You should be familiar with the following tools and their parameters:
  netstat
  nbtstat
  tracert or traceroute
  pathping

## Slide 2: Troubleshooting Router Issues
TCP/IP comes with a set of utilities that can help track down most TCP/IP related problems
You should be familiar with the following tools and their parameters:
  netstat
  nbtstat
  tracert or traceroute
  pathping
Notes: Troubleshooting Router Issues
TCP/IP comes with a set of utilities that can help track down most TCP/IP related problems
You should be familiar with the following tools and their parameters:
  netstat
  nbtstat
  tracert or traceroute
  pathping

## Slide 3: Troubleshooting Tools
netstat - displays TCP/IP statistics and details about TCP/IP components/connections on a host
  Information that can be obtained from the netstat command includes:
    The port on which a particular TCP/IP service is running
    Which network connections are currently established for a client
    How many messages have been handled by a network interface since it was activated
    How many data errors have occurred on a particular network interface
Notes: Troubleshooting Tools
netstat - displays TCP/IP statistics and details about TCP/IP components/connections on a host
  Information that can be obtained from the netstat command includes:
    The port on which a particular TCP/IP service is running
    Which network connections are currently established for a client
    How many messages have been handled by a network interface since it was activated
    How many data errors have occurred on a particular network interface

## Slide 4: Troubleshooting Tools
Notes: Troubleshooting Tools

## Slide 5: Troubleshooting Tools
nbtstat - provides information about NetBIOS statistics and resolve NetBIOS names to their IP addresses
  If you know the NetBIOS name of a workstation, you can use nbtstat to determine its IP address
  NetBIOS is a Windows protocol that was once an alternative to TCP/IP
    Mostly used by legacy applications
Notes: Troubleshooting Tools
nbtstat - provides information about NetBIOS statistics and resolve NetBIOS names to their IP addresses
  If you know the NetBIOS name of a workstation, you can use nbtstat to determine its IP address
  NetBIOS is a Windows protocol that was once an alternative to TCP/IP
    Mostly used by legacy applications

## Slide 6: Troubleshooting Tools
Notes: Troubleshooting Tools

## Slide 7: Troubleshooting Tools
tracert or traceroute -
  Windows tracert utility uses ICMP echo requests to trace the path from one networked node to another, identifying all intermediate hops between the nodes
  Linux, UNIX, and OS X system use the traceroute utility to send UDP messages to a random port on the destination node (concept is the same as tracert)
  Both utilities employ a trial-and-error approach to discover the nodes at each hop from source to destination
Notes: Troubleshooting Tools
tracert or traceroute -
  Windows tracert utility uses ICMP echo requests to trace the path from one networked node to another, identifying all intermediate hops between the nodes
  Linux, UNIX, and OS X system use the traceroute utility to send UDP messages to a random port on the destination node (concept is the same as tracert)
  Both utilities employ a trial-and-error approach to discover the nodes at each hop from source to destination

## Slide 8: Troubleshooting Tools
Notes: Troubleshooting Tools

## Slide 9: Troubleshooting Tools
Notes: Troubleshooting Tools

## Slide 10: Troubleshooting Tools
tracert or traceroute (cont’d) -
  A trace test might stop before reaching the destination for one of three reasons:
    The device the trace is attempting to reach is down
    It’s too busy to process lower-priority messages such as UDP or ICMP
    It does not accept the UDP or ICMP transmissions being sent because a firewall blocks these types of messages
  A trace cannot detect router configuration problems or predict variations of routes over a period of time
Notes: Troubleshooting Tools
tracert or traceroute (cont’d) -
  A trace test might stop before reaching the destination for one of three reasons:
    The device the trace is attempting to reach is down
    It’s too busy to process lower-priority messages such as UDP or ICMP
    It does not accept the UDP or ICMP transmissions being sent because a firewall blocks these types of messages
  A trace cannot detect router configuration problems or predict variations of routes over a period of time

## Slide 11: Troubleshooting Tools
pathping - a Windows utility that combines elements of both ping and tracert to provide deeper information about network issues along a route
  Sends multiple pings to each hope along a route, then compiles information into a single report
  A disadvantage of pathping is the amount of time it takes to run
    Shorten running type by limiting the number of queries per hop with the -q parameter
Notes: Troubleshooting Tools
pathping - a Windows utility that combines elements of both ping and tracert to provide deeper information about network issues along a route
  Sends multiple pings to each hope along a route, then compiles information into a single report
  A disadvantage of pathping is the amount of time it takes to run
    Shorten running type by limiting the number of queries per hop with the -q parameter

## Slide 12: Troubleshooting Tools
Notes: Troubleshooting Tools

## Slide 13: Solving Common Routing Problems
Notes: Solving Common Routing Problems

## Slide 14: Solving Common Routing Problems
Interface Errors - occur when a logical (not physical) connection between a node and a network is malfunctioning
  Two important guidelines when dealing with this problem:
    The ping command is a great place to start
    The netstat command can give you a list of interfaces on a device, and then can be used to troubleshoot network interface errors
Notes: Solving Common Routing Problems
Interface Errors - occur when a logical (not physical) connection between a node and a network is malfunctioning
  Two important guidelines when dealing with this problem:
    The ping command is a great place to start
    The netstat command can give you a list of interfaces on a device, and then can be used to troubleshoot network interface errors

## Slide 15: Solving Common Routing Problems
Hardware Failure - when a router, switch, NIC, or other hardware goes down
  Use tracert or traceroute to track down malfunctioning routers and other devices on larger networks
  Get more accurate trace feedback on a questionable router by targeting a node on the other side of that router, rather than aiming for that router itself
Notes: Solving Common Routing Problems
Hardware Failure - when a router, switch, NIC, or other hardware goes down
  Use tracert or traceroute to track down malfunctioning routers and other devices on larger networks
  Get more accurate trace feedback on a questionable router by targeting a node on the other side of that router, rather than aiming for that router itself

## Slide 16: Solving Common Routing Problems
Discovering Neighbor Devices - a process used by routers to learn about all of the devices on their networks
  On IPv4 networks, neighbor discovery is managed by ARP with help from ICMP
  IPv6 devices use Neighbor Discovery Protocol (NDP) to automatically detect neighboring devices and automatically adjust when neighboring nodes fail or are removed
    Eliminates the need for ARP and ICMP functions in IPv6 networks
Notes: Solving Common Routing Problems
Discovering Neighbor Devices - a process used by routers to learn about all of the devices on their networks
  On IPv4 networks, neighbor discovery is managed by ARP with help from ICMP
  IPv6 devices use Neighbor Discovery Protocol (NDP) to automatically detect neighboring devices and automatically adjust when neighboring nodes fail or are removed
    Eliminates the need for ARP and ICMP functions in IPv6 networks

## Slide 17: Solving Common Routing Problems
Path MTU Black Hole - messages are being lost for no apparent reason
  If suspected, use the ping command to determine the largest size message that can successfully traverse a path to its destination
    Adjust the buffer size of the ICMP echo message
    Start with a smaller buffer and work your way up to determine the largest MTU the route can handle
Notes: Solving Common Routing Problems
Path MTU Black Hole - messages are being lost for no apparent reason
  If suspected, use the ping command to determine the largest size message that can successfully traverse a path to its destination
    Adjust the buffer size of the ICMP echo message
    Start with a smaller buffer and work your way up to determine the largest MTU the route can handle

## Slide 18: Solving Common Routing Problems
Missing IP Routes - certain routes must be statically routed, such as gateway of last resort, routes to networks directly connected to the local network
  Sometimes these routes can become corrupted, outdated, or lost from the routing table
  Use the netstat -r command to display routing table
  Check that IP addresses are configured correctly for all interfaces
  Confirm that none of the affected routers are in passive-interface mode
Notes: Solving Common Routing Problems
Missing IP Routes - certain routes must be statically routed, such as gateway of last resort, routes to networks directly connected to the local network
  Sometimes these routes can become corrupted, outdated, or lost from the routing table
  Use the netstat -r command to display routing table
  Check that IP addresses are configured correctly for all interfaces
  Confirm that none of the affected routers are in passive-interface mode

## Slide 19: Summary
A router is a multiport device that can connect dissimilar LANs and WANs running at different transmission speeds, using a variety of protocols
Static routing is when a network administrator programs a router to use specific paths between nodes
To determine best path, routers communicate with each other through routing protocols
Routing metrics may factor in the number of hops between nodes, throughput, delay, MTU, cost, load, and reliability
Notes: Summary
A router is a multiport device that can connect dissimilar LANs and WANs running at different transmission speeds, using a variety of protocols
Static routing is when a network administrator programs a router to use specific paths between nodes
To determine best path, routers communicate with each other through routing protocols
Routing metrics may factor in the number of hops between nodes, throughput, delay, MTU, cost, load, and reliability

## Slide 20: Summary
RIP, a distance-vector routing protocol, is the slowest and least secure routing protocol
OSPF is a link-state routing protocol used on interior or border routers
IS-IS uses virtually the same methods as OSPF to calculate paths but is less common
BGP uses the most complex best-path calculation of all commonly used routing protocols
The netstat utility displays TCP/IP statistics and the state of current TCP/IP components
Notes: Summary
RIP, a distance-vector routing protocol, is the slowest and least secure routing protocol
OSPF is a link-state routing protocol used on interior or border routers
IS-IS uses virtually the same methods as OSPF to calculate paths but is less common
BGP uses the most complex best-path calculation of all commonly used routing protocols
The netstat utility displays TCP/IP statistics and the state of current TCP/IP components

## Slide 21: Summary
The nbtstat utility provides information about NetBIOS names and their addresses
The traceroute utility, known as tracert on Windows-based system, uses ICMP to trace the path from one networked node to another
The route command allows you to view a host’s routing table and add, delete, or modify preferred routes
Notes: Summary
The nbtstat utility provides information about NetBIOS names and their addresses
The traceroute utility, known as tracert on Windows-based system, uses ICMP to trace the path from one networked node to another
The route command allows you to view a host’s routing table and add, delete, or modify preferred routes